3GPP TSG RAN Meeting #69	RP-151606

# Phoenix, USA, 14 – 16 September 2015

# Source:	Samsung, Nokia Networks

# Title:	New SID Proposal: Study on channel model for frequency spectrum above 6 GHz

# Document for:	Approval

Agenda Item:	14.1.1

3GPP™ Work Item Description

For guidance, see 3GPP Working Procedures, article 39; and 3GPP TR 21.900.
Comprehensive instructions can be found at http://www.3gpp.org/Work-Items

# Title:	Study on channel model for frequency spectrum above 6 GHz

## Acronym: FS_CM_Above6GHz

## Unique identifier:

NOTE:	If this is a RAN WID including Core and Perf. part, then Title, Acronym and Unique identifier refer to the feature WI. Please tick (X) the applicable box(es) in the table below:

| This WID includes a Core part |  |
| --- | --- |
| This WID includes a Performance part |  |

## 1	3GPP Work Area

| X | Radio Access |
| --- | --- |
|  | Core Network |
|  | Services |

## 2	Classification of WI and linked work items

### 2.0	Primary classification

This work item is a …

| x | Study Item (go to 2.1) |
| --- | --- |
|  | Feature (go to 2.2) |
|  | Building Block (go to 2.3) |
|  | Work Task (go to 2.4) |

NOTE:	Core, Performance and Testing parts of RAN WIs are usually Building Blocks.
If you are in doubt, please contact MCC.

### 2.1	Study Item

| Related Work Item(s) (if any] |
| --- |
| Unique ID | Title | Nature of relationship |

Go to §3.

### 2.2	Feature

| Related Study Item or Feature (if any) |
| --- |
| Unique ID | Title | Nature of relationship |

Go to §3.

### 2.3	Building Block

| Parent Feature (or Study Item) |
| --- |
| Unique ID | Title | TS |

This work item is …

|  | Stage 1 (go to 2.3.1) |
| --- | --- |
|  | Stage 2 (go to 2.3.2) |
|  | Stage 3 (go to 2.3.3) |
|  | Test spec (go to 2.3.4) |
|  | Other (go to 2.3.5) |

#### 2.3.1	Stage 1

| Source of external requirements (if any) |
| --- |
| Organization | Document | Remarks |

Go to §3.

#### 2.3.2	Stage 2

| Corresponding stage 1 work item |
| --- |
| Unique ID | Title | TS |

| Other source of stage 1 information |
| --- |
| TS or CR(s) | Clause | Remarks |

If no identified source of stage 1 information, justify:

Go to §3.

#### 2.3.3	Stage 3

| Corresponding stage 2 work item (if any) |
| --- |
| Unique ID | Title | TS |

| Else, corresponding stage 1 work item |
| --- |
| Unique ID | Title | TS |

| Other justification |
| --- |
| TS or CR(s) or external document | Clause | Remarks |

If no identified source of stage 2 information, justify:

Go to §3.

#### 2.3.4	Test spec

| Related Work Item(s) |
| --- |
| Unique ID | Title | TS |

Go to §3.

#### 2.3.5	Other

| Related Work Item(s) |
| --- |
| Unique ID | Title | Nature of relationship | TS / TR |

Go to §3.

### 2.4	Work task

| Parent Building Block |
| --- |
| Unique ID | Title | TS |

## 3	Justification

Since introduction of LTE and LTE-Advanced, 3GPP radio access technologies have been able to accommodate the increasing demand of wireless traffic. Carrier aggregation, which is one of the most important features in LTE-Advanced, is playing an important role to meet such capacity demand by utilization of up to 100MHz.

It is a common expectation in mobile industry that there will be exponential increase of capacity demand and hence even larger bandwidth than 100MHz would need to be used. There is huge on-going effort in industry as well as academia to investigate the feasibility of using around 1GHz bandwidth in the frequency range above the current cellular spectrum. ITU-R WP5D sent a LS to 3GPP in RP-140401 informing that they are performing the study on technical feasibility of IMT in the bands above 6 GHz.

Taking into account the various activities and consideration as above, 3GPP, as the leading standard body for mobile technologies, would need to study performance and feasibility of using high frequency spectrum above 6 GHz for further evolution beyond LTE-Advanced and for technology advancement towards 5G.

## 4	Objective

### 4.1	Objective of SI or Core part WI or Testing part WI

The study item aims to develop a channel model to enable feasibility study and developing framework of using high frequency spectrum ranging from 6 GHz to 100 GHz. In order to achieve this, the study item should fulfil the following objectives.

- From RAN#69 (Sep 2015) to RAN#70 (Dec 2015), RAN identifies the status/expectation of existing information on high frequencies (e.g. spectrum allocation, scenarios of interest, measurements, etc).

- There would be email discussion between RAN#69 and RAN#70. A session will take place in RAN#70 to wrap-up the outcomes of email discussion.

- From Q1 2016, RAN1 develops a channel model(s) for frequencies up to 100 GHz taking into account the outcome of RAN-level discussion and discussion in the ‘5G’ requirement study item.

  - Define the additional details of the scenarios of interest required for RAN1 work

  - Consider the work done outside 3GPP as well as earlier 3GPP work, such as the 3GPP 3D-channel model, as a starting point for modelling of wireless channels of the high frequency spectrum for the identified scenarios.

  - Consider possible implication of the new channel model on the existing 3D channel model for below 6 GHz.

### 4.2	Objective of Performance part WI

NOTE:	Leave empty if the WI proposal does not contain a RAN performance part.

### 4.3	RAN time budget proposal

NOTE:	For Wis/Sis under RAN WG5 leadership this section is not filled out. Otherwise:
For a not yet approved WI/SI the rapporteur has to fill out the last row of the table(s) below up to the target date of the WI/SI (if necessary add further tables): Indicate the number of time units (1 TU ~ 2h), i.e. one value for each session/field. If no time unit is needed, leave the field empty.
Once the WI/SI is approved, the tables below will no longer be updated in the WI/SI description (i.e. the tables reflect the status of the initial approval). But changes can be proposed in the status report of the WI/SI.

From RAN#69 to RAN#70, RAN-level email discussion will take place, which will be followed by a session in RAN#70.

| RAN #70 Q1/2016 RAN #71 |
| --- |
| R1L | R1U | R2L | R2U | R2J | R3 | R4RF Core | R4RD Core | R4RF Perf | R4RD Perf |
| 84 | 84 | 93 | 93 | 93 | 91 | 78 | 78 | 78 | 78 |
| 2 |  |  |  |  |  |  |  |  |  |

| RAN #71 Q2/2016 RAN #72 |
| --- |
| R1L | R1U | R2L | R2U | R2J | R3 | R4RF Core | R4RD Core | R4RF Perf | R4RD Perf | R1L | R1U | R2L | R2U | R2J | R3 | R4RF Core | R4RD Core | R4RF Perf | R4RD Perf |
| 84bis | 84bis | 93bis | 93bis | 93bis | 91bis | 78bis | 78bis | 78bis | 78bis | 85 | 85 | 94 | 94 | 94 | 92 | 79 | 79 | 79 | 79 |
| 3 |  |  |  |  |  |  |  |  |  | 3 |  |  |  |  |  |  |  |  |  |

NOTE:	In case further explanation of the time budget proposal is needed, then please explain this below.

Additional comments to the time budget proposal:

The TU allocation table is subject to the final decision of completion date.

This SI will not be subject to the regular RAN prioritization, it will be done in parallel to the existing RAN WG work/capacity (no TU’s discussion; no schedule constraints due to the existing work).

## 5	Service Aspects

## 6	MMI-Aspects

## 7	Charging Aspects

## 8	Security Aspects

## 9	Impacts

| Affects: | UICC apps | ME | AN | CN | Others |
| --- | --- | --- | --- | --- | --- |
| Yes |  | X | X |  |  |
| No | X |  |  | X | X |
| Don’t know |  |  |  |  |  |

## 10	Expected Output and Time scale

| New specifications [If Study Item, one TR is anticipated] |
| --- |
| Spec No. | Title | 1st rsp. WG | 2nd rsp. WG(s) | Presented for information at plenary# | Approved at plenary # | Comments |
| TR36.xxx | Study on channel model for frequency spectrum above 6 GHz | RAN1 |  | [RAN#71] | [RAN#72] | Planned completion date will be reviewed in future TSG RAN meetings taking into account the expected work to be done and actual progress. |

NOTE:	If this is a RAN WID including Core and Perf. Part, then all new Core part specs have to be listed first and then all new Perf. Part specs. Indicate “Core part” or “Perf. Part” under Comments for each spec.
By default a new specs can only be new for one of both parts.

| Affected existing specifications [None in the case of Study Items] |
| --- |
| Spec No. | CR | Subject of the CR | Approved at plenary# | Comments |

NOTE:	If this is a RAN WID including Core and Perf. Part, then all new Core part specs have to be listed first and then all new Perf. Part specs. Indicate “Core part” or “Perf. Part” under Comments for each spec.
If an existing spec is affected by both (Core part and Perf. Part), then it has to be listed twice with appropriate approval dates.

## 11	Work item rapporteur(s)

Charlie Zhang

Company:	Samsung

Email:	jianzhong.z@samsung.com

Xiaoyi Wang

Company:	Nokia Networks

Email:	xiaoyi.wang@nokia.com

## 12	Work item leadership

RAN1

NOTE:	If this is a RAN WID including Core and Perf. Part, then this WG specifies the WG leading the Core part.
RAN WG4 is by default leading the Perf. Part.

## 13	Supporting Individual Members

Supporting IM name

Alcatel Lucent

Alcatel Lucent Shanghai Bell

Samsung

Nokia Networks

AT&T

Dish Network

Deutsche Telekom

ETRI

Ericsson

Fujitsu

HiSilicon

Huawei

Intel Corporation

InterDigital

KDDI

Keysight Technologies

KT Corp.

Lenovo

LG Electronics

Mitsubishi Electric Corporation

Motorola Mobility

NEC

NTT DOCOMO

Oppo

Panasonic

Qualcomm

Rohde and Schwarz

SK Telecom

Spirent Communications

Sprint

Straight Path

Verizon

ZTE Corporation

form change history:

2013-12-06 v1.14.1 modified §11 to read: <FamilyName>, <GivenName>, (If the person is new to 3GPP work, give full contact coordinates, in particular, email address.)

2013-10-03 v1.14.0 removal of embedded help text

v1.13.2: adds tdoc header

v1.13.1: minor changes resulting from discussions at CT#41 & SA#41

v1.13.0: mods to enforce linkage amongst stages 1, 2, 3

draft mods Scarrone-Meredith 2008-07 ff

v1.12.1: removes revision marks following approval at SP-29
v1.12.0: includes provision for Study Items (SP-29)

v1.11.0: includes those changes from v1.8.0 agreed at SP-25.

v1.10.0: full circle

v1.9.0: a clean sheet

v1.8.0: includes comments from SA#24

v1.7.0: includes comments from RAN, CN and T #24; also includes “early implementation” data

v1.6.0: includes comments made during review period prior to TSGs#24

v1.5.0: includes comments made at TSGs#23 (Phoenix)

v1.4.0: offered to SA#23 for approval

v1.3.0: offered to CN#23, RAN#23 and T#23 for comments

DRAFT4 v1.3.0: 2004-03-09: Incorporation of comments from Leaders list

DRAFT3 v1.3.0: 2004-02-19: Incorporation of comments from MCC members

DRAFT2 v1.3.0: 2004-01-29: Complete redraft:

v1.2.0: 2002-07-04: "USIM" box changed to "UICC apps"

2003-05-28: spelling of “rapporteur” corrected

2002-07-04: "USIM" box changed to "UICC apps"